## Slide 1: Timing Jitter and Cross Talk in the SRS + Xray scan of FIT zigzag board Michael Phipps, Bob Azmoun, and Craig Woody

## Slide 2: External Pulser Test Setup Data taken from external pulser coupled directly to a single strip and processed through the SRS
Two channels of function generator synched. One sent to 3 pF capacitor. Other to SRS trigger.
Readout board covered by anti-static bag. Entire system wrapped in aluminum foil.
Compass board grounded. APV covered in electrical tape. Grounding strips added.
Twisted pair soldered directly to readout strip and ground

## Slide 3
Timing Jitter: 8.765 ns
Pedestal-subtracted (unsaturated/nonlinearity corrected) ADC averaged across remaining time bins from each pulse. Taken with the Compass board
Average sigma: 0.3506 time bins
or 8.765 ns
Also a 25 ns shift in every 6 or 7 events. Contributes to background noise in residual plots. Where does this come from? 1 time bin jitter in APV analog pipeline?

## Slide 4
Xray Gun
External Pulser
Secondary Peak:
Is it SRS related or introduced by external pulser?
Not there?
Not conclusive

## Slide 5: Cross Talk: ~7.5% Pulse height of right and left neighboring strips relative to primary strip. Charge injected directly on primary strip from external pulser. Any signal on neighbors a result of capacitive coupling. Tested on 0.4 mm pitch Compass readout board.
Left/right neighbor show same coupling
Amplitude cross talk dependency not significant – any differences due to lower events at 7 mV being lost in noise
Cross talk for compass board w/ SRS readout: ~7.5%

## Slide 6: Xray scan of FIT 48 strip 1d zigzag board Data taken in 100 um steps across ~2 mm zigzag pattern with collimated xray gun

## Slide 7
Behavior of FIT Zigzag pattern

## Slide 8: Finding the Correction Function
Subtract off motor position of xray gun

## Slide 9
Full Pad Function
Half Pad Function
Corrected Half Pad Function
5 Pad Events
6 Pad Events

## Slide 10
FIT 48 strip 1d zigzag board
BNL 2d chevron board

## Slide 11
Corrected Resolution at first R value
Using same correction function for all events
Using separate 5/6 pad correction functions
Corrected: 110 um
Uncorrected: 140 um
Corrected: 168.9 um
Uncorrected: 267.0 um
Corrected: 182.4 um
Uncorrected: 267.0 um
FIT board
BNL board